## Slide 1: 1000 VDC/60−125 A Auto Grade Fuse EV1K Series
New Product Introduction

## Slide 2: EV1K Series Fuse 1000 VDC/60–125 A Auto Grade
Problem/Solution
The EV1K Series Fuse is designed specifically for automotive-grade solutions applications. It provides overcurrent protection in applications connected to Electric Vehicles' high voltage power supply. With a rating of 1000 Vdc, the fuse is currently available in amperage ratings of 60 to 125 A (ratings up to 600 A are forthcoming). It uses a bolt-down form factor with a 25 mm x 73 mm cartridge body. The certification testing for this fuse uses the ISO 8820 and LV standards to ensure it is compatible with the Automotive environment (thermal shock/cycling, vibration, etc.).
Features
Rated for 1000 Vdc with interrupting rating of 30,000 A and 60−125 A nominal amperage ratings in bolt-down package
End caps with integrated bolt-down terminals
Compact body size of 25x73 mm
Operating temperature range from -40 ºC to 125 ºC
Benefits
Durable against mechanical vibration and shock, which increases product life and longevity
High interrupt rating and open state resistance for compatibility with short circuit protection
Resistance to thermal shock to handle temperature fluctuations for reliable cycling performance
Temperature and humidity-resistant to withstand a wide variety of environmental conditions
Markets/Applications
EV Power Circuits including:
  On-board charger
  Battery pack/distribution unit
  DC/DC converter
  Traction motor inverter
Technical resources (Click on below icons to learn more)
Tech Info
Datasheet
Series Page
Recommended Fuse Blocks
LSCR001 (60–125 A)
LSCR002 (150–600 A)
DC/DC Converter
On Board Charger
High Voltage Battery Pack
Battery Distribution Unit
Traction Motor Inverter
Ancillary Loads

## Slide 3: Target markets and applications
Markets | Applications | Select OEMs and Tier 1 Suppliers | Geography
Electric and Hybrid Passenger Cars | On Board Charger, DC/DC Converter, Battery Pack and Distribution Unit, Traction Motor and Ancillary Loads | General Motors, Ford, Tesla, Stellantis, Continental, Lear, LG Energy, CATL, BYD, Delta, Yazaki | Global
Commercial Vehicle (Truck, Bus, etc.) Heavy-Duty Hybrid and Electric | On Board Charger, DC/DC Converter, Battery Pack and Distribution Unit, Traction Motor and Ancillary Loads | Daimler, Mercedes-Benz, Volvo, Nikola, Tesla, Mitsubishi, Kenworth-Toyota, BYD, Proterra, Tata Motors | Global
Off-Highway (Construction, Agriculture) Hybrid and Electric Vehicles | On Board Charger, DC/DC Converter, Battery Pack and Distribution Unit, Traction Motor and Ancillary Loads | Cummins, John Deere, Caterpillar, Volvo, Komatsu, JCB, Bobcat, Hyundai, Monarch Tractor, Mahindra | Global
Electric Vehicle Infrastructure | AC Chargers and DC Chargers | ChargePoint, EV Box, BYD, Blink Charging, ABB, Eaton | Global

## Slide 4: EV1K fuse for EV battery pack protection
Click on the product series in the table below for more info
Technology |  | Product Series
1 | SMD Fuse | 501A, 881A
 | TVS Diode | TPSMC, SZ1SMC, SZ1.5SMC
2 | SMD or In-line Fuse | 438A, 441A, 521
 | TVS Diode | TPSMB, SZ1SMB, SZP6SMB
3 | Diode Array | AQ05C
 | TVS Diode | TPSMA6L, SZ1SMA
4 | High-voltage fuse | EV1K
5 | Gate Driver | IXD_6xxSI
6 | Diode Array | AQ24CANA
 | Fuse | 885
 | TVS Diode | TPSMB, TPSMC
Acronyms:
MOV: metal oxide varistor
TVS: transient voltage suppressor
SMD: surface mount device
Output
Pack 1
Module 2
Li-ion Cell pack
Cell balancing & control
Module
Li-ion Cells
Cell balancing & control
Module n
Li-ion Cell pack
Cell balancing & control
Pack X
Module 2
Li-ion Cell pack
Cell balancing & control
Module 1
Li-ion Cell pack
Cell balancing & control
Module n
Li-ion Cell pack
Cell balancing & control
Control & protect circuit
Battery system controller
Legend:
Power
Data
Contractor main switch
High voltage main fuse
3
3
1
2
1
2
5
6
4
NEW

## Slide 5: Battery distribution unit block diagram
 | Technology | Series
1 | Pre-Charge Contactor | DCNSEV, DCNLEV
2 | Main Positive Contactor | DCNEV
3 | Auxiliary Fuse | EV1K
4 | Auxiliary Contactor | DCNEV, DCNLEV
5 | Main Negative Contactor | DCNEV
6 | Pyro Safety Module | PSM*
Battery distribution unit
Battery pack
+
−
MCU
PTC Heater
Converter
Inverter
A/C Compressor
Others
Main Neg/Fast Charger-
Main Pos/Fast Charger+
1
2
3
4
5
* Please contact Littelfuse Associates for details
Click on the product series in the table below for more info
6
NEW

## Slide 6: On-board charger block diagram
Technology |  | Series
I | Fuse | 10EV*, 20EV
 | MOV | AUMOV
 | GDT | CG2, CG3
 | SIDACtor | Pxxx0FNL, Pxxx0SD
II | Thyristor | S8016xA
III | Gate Driver | IXD_6xxSI, IX4340NE
IV | TVS Diode | TPSMB, SZ1SMB, SZP6SMB
V | Gate Driver | IXD_6xxSI, IX4340NE
 | TVS Diode | TPSMB, SZ1SMB, SZP6SMB
 | Diode Array | AQ4022
VI | Fuse | EV1K
 | MOV | AUMOV
 | TVS Diode | TPSMB, SZ1SMB, SZP6SMB
VII | Diode Array | AQ24CANA
AC
AC
Cable
Input
voltage
Stationary
base
P
N
PE
OR
EMI
Filter
Rectifier
Power factor correction
DC
link
Output
voltage
DC/DC converter
II
III
I
IV
V
VI
Control unit
VII
* Please contact Littelfuse Associates for details
Click on the product series in the table below for more info
NEW

## Slide 7: Off-highway electric vehicle powertrain architecture
 | Technology | Product series
3 | Ignition Switch | 95060
 | High-current Fuse | ZCase
 | Fuse Block | FHZ
 | TVS Diode | SLD8S
 | DC Power Distribution Module | HWB60, HWB18
 | Manual Battery Disconnect Switches | 08010100, 08099100
4 | TVS Diode Array | AQ24CANA
 | TVS Diode | TPSMB, SZ1SMB, SZP6SMB
 | Gate Driver | IXD_6xxSI, IX4340NE, IX4351NE
 | Si/SiC MOSFET | X Class, X2 Class, LSIC1MOxx
 | Diode | DSEP,LSIC2SD, DHG
5 | TVS Diode Array | AQ24CANA
 | TVS Diode | TPSMB
 | Gate Driver | IXD_6xxSI, IX4340NE, IX4351NE
 | IGBT Discrete (1200 V, 150 A) | Trench XPTTM , Planar
 | IGBT Module (1200 V, 450 A) | MIXA450PF1200TSF
6 | DC output Fuse | EV1K
 | HV DC Contactor Relays | DCNEV, DCNLEV
 | Power Distribution Module | MDB5
Click on the product series in the table below for more info
* Please contact Littelfuse Associates for details
On-Board charger
12V battery
+ PDU
DC/DC
converter
AC
compressor
Electric
PTO motor
Traction motor inverter
Drive
motor
Electric
PTO motor
Battery pack
+ BMS
PTC
heater
Charging cord
Junction
box
1
2
3
4
6
Legend:
Low/High-voltage DC
AC input voltage
BMS: Battery Management System
PDU: Power Distribution Unit
PTO: Power Take-off
PTC: Positive Temperature Coefficient
5
NEW

## Slide 8: DC Charger cabinet level protection
 | Technology | Series
1 | Fuse x 3 | PSR, L50QS, L75QS
2 | Ground Fault Relay | SE-704, SE-CS30
3 | AC Contactor | HCD
4 | AC Relay | SC0x*
5 | Fuse + Fuseholder | LVSP + LPSM
6 | Surge Protection Device | SPD Type 2
7 | DC Contactor Relay | DCNxx
8 | Fuse x 2 | SFPJ, PSR, EV1K
1
3
5
7
2
4
6
8
AC main
RCD high immunity
Power converter
Power converter
Power converter
Power converter
Isolation monitoring
Isolation monitoring
Control
Communication interface
(PLC, 5G, Zigbee, RS-485, Ethernet)
CCS
CHAdeMO
Tº
Tº
Temperature sensing
Control pilot proxy
Main isolator
24 V Aux PSU
Heater
AC
DC
Acronyms:
RCD: Residual Current Device
CCS: Constant Current Source
PLC: Programmable Logic Controller
CHAdeMO: DC charging protocol currently enabling EV charging with power from 6 kW to 400 kW with 900 kW in preparation
Click on the product series in the table below for more info
* Please contact Littelfuse Associates for details
NEW
1
2
3
4
5
6
7
8

## Slide 9: Comparison of EV1K Series with existing Littelfuse products
Parameter | EV1K | 20EV | 828
Product Photo |  |  | 
Footprint/Height | 73 x Φ 25 mm | 42 x Φ 20 mm | 38 x Φ 10 mm
Voltage Rating | 1000 VDC | 500 VDC | 1000 VDC
Interrupting Rating | 30 kA @ 1000 VDC | 16 kA @ 500 VDC | 10 kA @ 1000 VDC
Amperage Rating | 60 A to 125 A (under development up to 600 A) | 60 A to 125 A | 15 A ~ 30 A
Operating Temperature | -40 °C to +125 °C | -40 °C to +125 °C | -55 °C to +125 °C
Agency Approval | ISO8820, JASO D622 | ISO8820, JASO D622 | 
Key advantages over the existing product series
Rated for 1000 VDC with interrupting rating of 30,000 A and 60−125 A nominal amperage ratings in bolt-down package
Compact body size of 25x73 mm
Operating temperature range from -40 ºC to 125 ºC

## Slide 10: Comparison of EV1K series with competition
Parameter | EV1K | Mxx MEV100 Series
Product Photo |  | 
Voltage Rating | 1000 VDC | 1000 VDC
Interrupting Rating | 30 kA @ 1000 VDC | 20 kA @ 1000 VDC
Amperage Rating | 60 A to 600 A (currently available only up to 125 A) | 50 A to 600 A
Operating Temperature | -40 °C to +125 °C | -40 °C to +125 °C
Agency Approval | ISO8820 JASO D622 | ISO8820 JASO D622

## Slide 11: Pricing, samples, availability and contacts
Pricing and samples |  | 
Please contact Littelfuse product management and sales representatives for pricing and samples availability. |  | 
Product availability |  | 
Production lead-time | 16 weeks | 
Packaging | Tray | 
Contact details |  | 
Product Manager | Ben Zheng | bzheng@littelfuse.com
Asst. Product Manager | Sakthidharan Krishnamoorthy | SKrishnamoorthy@littelfuse.com
Product Engineer | Ray Zumbahlen | RZumbahlen@littelfuse.com

## Slide 12: Sales tools, technical support and keywords
Current datasheets are available on www.littelfuse.com.
Enter EV1K in the search box.
Application and Technical Support: 1-800-999-9445
Suggested Keywords
  Overcurrent Protection
  Electric Vehicles
  Electric Vehicle Infrastructure
  On Board Charger
  Traction Motor Inverter
  High Voltage Battery Pack
  Battery Disconnect Unit
  DC/DC Converter
  Off Highway Vehicles
  High Voltage Automotive Fuse
  xEV Fuse
  EV Fuse
  Electric Vehicle Fuse

## Slide 13: Local resources supporting our global customers
Manaus
São Paulo
Fremont
Milpitas
Long Beach
Rapid City
Saskatoon
Burlington
Mount Prospect
Madison
Chicago
Troy
Champaign
Rock Falls
Beverly
Piedras Negras
Matamoros
Muzquiz
Charneca de Caparica
San Sebastian
Legnago
Beijing
Wuxi
Suzhou
Shanghai
Kunshan
Tsukuba
Tokyo
SeongnamSeoul
Chu-pei
Taguig
Lipa City
Taipei
Singapore
Dongguan
Shenzhen
Hong Kong
Kaunas
Amsterdam
Deventer
Sales
Legend
R&D
Manufacturing
Bremen
Lampertheim
Essen
Lauf
Chippenham
New Delhi
Round Rock

## Slide 14: Partner for tomorrow’s electronic systems
An industrial technology manufacturing company empowering a sustainable, connected, and safer world
BROAD
PRODUCT PORTFOLIO
Our engineers partner directly with customers to help speed up product design and meet their unique needs
APPLICATION
EXPERTISE
Our global customer service team is with you to anticipate your needs and ensure a seamless experience
GLOBAL
CUSTOMER SERVICE
To help customers in the design process to account for requirements set by global regulatory authorities
COMPLIANCE AND
REGULATORY EXPERTISE
To help customers get products to market faster, we offer certification testing to global regulatory standards
TESTING
CAPABILITIES
High-volume manufacturing that is committed to the highest quality standards
GLOBAL
MANUFACTURING

## Slide 15
Littelfuse.com
This document is provided by Littelfuse, Inc. (“Littelfuse”) for informational and guideline purposes only. Littelfuse assumes no liability for errors or omissions in this document or for any of the information contained herein. Information is provided on an “as is” and “with all faults” basis for evaluation purposes only. Applications described are for illustrative purposes only and Littelfuse makes no representation that such applications will be suitable for the customer’s specific use without further testing or modification. Littelfuse expressly disclaims all warranties, whether express, implied or statutory, including but not limited to the implied warranties of merchantability and fitness for a particular purpose, and non-infringement. It is the customer’s sole responsibility to determine suitability for a particular system or use based on their own performance criteria, conditions, specific application, compatibility with other components, and environmental conditions. Customers must independently provide appropriate design and operating safeguards to minimize any risks associated with their applications and products. Read complete Disclaimer Notice at: www.littelfuse.com/disclaimer-electronics.